## Slide 1: Finite element programming with Matlab
Lecture-14
Dr. Reem Alsehnawi
MATLAB Codes for Finite Element Analysis
(2D Trusses)

## Slide 2
2D Trusses:

## Slide 3
Stiffness Matrix:
In the local coordinate system,
the global stiffness matrix
Stresses at the Element:
Stresses in the global coordinates as function of the displacements:

## Slide 4
2D truss problem:
As illustrated in the figure, we consider a downward point force (10,000) applied at node 1. The modulus of elasticity is E = 30e6 and all elements are supposed to have constant cross-section area A = 2. The supports are located in nodes 2 and 4.

## Slide 5
2D truss problem: ( Matlab Code)
% clear memory
clear all
% E; modulus of elasticity
% A: area of cross section
% L: length of bar
E=30e6; A=2; EA=E*A;
% generation of coordinates and connectivities
numberElements=3;
numberNodes=4;
elementNodes=[1 2;1 3;1 4];
nodeCoordinates=[ 0 0;0 120;120 120;120 0];
xx=nodeCoordinates(:,1);
yy=nodeCoordinates(:,2);

## Slide 6
2D truss problem: ( Matlab Code)
% for structure:
% displacements: displacement vector
% force : force vector
% stiffness: stiffness matrix
GDof=2*numberNodes; % GDof: total number of degrees of freedom
displacements=zeros(GDof,1);
force=zeros(GDof,1);
% applied load at node 2
force(2)=-10000.0;
% computation of the system stiffness matrix
[stiffness]=...
formStiffness2Dtruss(GDof,numberElements,...
elementNodes,numberNodes,nodeCoordinates,xx,yy,EA);

## Slide 7
2D truss problem: ( Matlab Code)
% boundary conditions and solution
prescribedDof=[3:8]’;
% solution
displacements=solution(GDof,prescribedDof,stiffness,force);
% stresses at elements
stresses2Dtruss(numberElements,elementNodes,...
xx,yy,displacements,E)
% output displacements/reactions
outputDisplacementsReactions(displacements,stiffness,...
GDof,prescribedDof)

## Slide 8
2D truss problem: ( Matlab Code)
function [stiffness]=...
formStiffness2Dtruss(GDof,numberElements,...
elementNodes,numberNodes,nodeCoordinates,xx,yy,EA);
stiffness=zeros(GDof);
% computation of the system stiffness matrix
for e=1:numberElements;
% elementDof: element degrees of freedom (Dof)
indice=elementNodes(e,:) ;

## Slide 9
2D truss problem: ( Matlab Code)
elementDof=[ indice(1)*2-1 indice(1)*2 indice(2)*2-1
indice(2)*2] ;
xa=xx(indice(2))-xx(indice(1));
ya=yy(indice(2))-yy(indice(1));
length_element=sqrt(xa*xa+ya*ya);
C=xa/length_element;
S=ya/length_element;
k1=EA/length_element*...
[C*C C*S -C*C -C*S; C*S S*S -C*S -S*S;
-C*C -C*S C*C C*S;-C*S -S*S C*S S*S];
stiffness(elementDof,elementDof)=...
stiffness(elementDof,elementDof)+k1;
end

## Slide 10
2D truss problem: ( Matlab Code)
function stresses2Dtruss(numberElements,elementNodes,...
xx,yy,displacements,E)
% stresses at elements
for e=1:numberElements
indice=elementNodes(e,:);
elementDof=[ indice(1)*2-1 indice(1)*2 indice(2)*2-1
indice(2)*2] ;
xa=xx(indice(2))-xx(indice(1));
ya=yy(indice(2))-yy(indice(1));
length_element=sqrt(xa*xa+ya*ya);
C=xa/length_element;
S=ya/length_element;
sigma(e)=E/length_element* ...
[-C -S C S]*displacements(elementDof);
end
disp(’stresses’)
sigma’

## Slide 11
2D truss problem: ( Matlab Code)
Displacements
ans =
1.0000 0.0041
2.0000 -0.0159
3.0000 0
4.0000 0
5.0000 0
6.0000 0
7.0000 0
8.0000 0
reactions
ans =
1.0e+03 *
0.0030 0
0.0040 7.9289
0.0050 2.0711
0.0060 2.0711
stresses
ans =
1.0e+03 *
3.9645
1.4645
-1.0355
Deformed shape

## Slide 12
2D truss problem: ( Matlab Code)
Deformed shape
% drawing displacements
us=1:2:2*numberNodes-1;
vs=2:2:2*numberNodes;
figure
L=xx(2)-xx(1);
%L=node(2,1)-node(1,1);
XX=displacements(us);YY=displacements(vs);
dispNorm=max(sqrt(XX.^2+YY.^2));
scaleFact=15000*dispNorm;
clf
hold on
drawingMesh(nodeCoordinates+scaleFact*[XX YY], elementNodes, ’L2’, ’k.-’);
drawingMesh(nodeCoordinates,elementNodes,’L2’,’k.--’);

## Slide 13
Homework (2D truss with spring)
The figure consider a structure that is built from two truss elements and one spring element. For the truss elements the modulus of elasticity is E = 210 GPa, and the cross-section area is A = 5e−4 m2. This problem is modeled with four points and three elements. Write Matlab Code.